# Text boxes

PREFLIGHT

COCKPIT

Required Documents	ABOARD

Fuel Level		Check

FUSELAGE (Left Side)

Static Port		OPEN

EMPENNAGE

Control Surfaces		CHECK

Tie Down		REMOVE

Tail Wheel		CHECK

FUSELAGE (Right Side)

Static Port		OPEN

Comm Antenna 		CHECK

RIGHT WING

Control Surfaces		CHECK

Tie-Down		REMOVE

Tire / Brake		CHECK

NOSE

Cowl Covers		REEMOVE

Transponder Antenna	CHECK

Muffler			CHECK

Gascolator		DRAIN

Sample			CHECK

Cowling			CHECK

Propeller / Spinner		CHECK

Oil Quantity		CHECK

Oil Door			CLOSED

LEFT WING

Pitot Tube		CHECK

Tie-Down		REMOVE

Control Surfaces		CHECK

Tire / Brake		CHECK

BEFORE STARTING ENGINE

Passengers	                BRIEFED

Seat Belt/Shoulder Harness    FASTENED

Fuel Valve	                FULLEST TANK

Brakes		                HOLD

Batt. / Master	              ON

STARTING ENGINE - COLD

Throttle			¼ OPEN

Mixture   		FULL RICH

Boost Pump		ON 2-3 Sec.

Boost Pump 		OFF

Throttle			½ INCH OPEN

Propeller Area		Clear

Ignition Switch		START

Idle			800 – 1000

Oil Pressure		CHECK

Mixture			LEAN, TAXI

Avionics Master		ON

Strobes			ON

LDG Lights		WIGWAG

BEFORE TAKE OFF

Flight Controls	FREE & CORRECT

Flight Instruments	SET

Fuel Valve	FULLEST TANK

All Trim Tabs	SET FOR TAKEOFF

Throttle (Friction Set)	1700 RPM

- Mags	CHECK

- Oil Pres/Temp	CHECK/GREEN

- Ammeter 	CHECK

Mixture	AS REQUIRED

Radios	SET

Transponder	ALTITUDE

Seat Belt / Harness	TIGHT

Canopy	SECURE

Flaps	UP

TAKE OFF

Flaps			SET

Throttle			FULL OPEN

STARTING ENGINE - HOT

***DO NOT PRIME***

Mixture			IDLE CUT-OFF

Boost Pump		OFF

Throttle			½ INCH OPEN

Propeller Area		Clear

Ignition Switch		START

Mixture			ADVANCE

Idle			800 – 1000

Oil Pressure		CHECK

Mixture			LEAN, TAXI

Avionics Master		ON

Lights			ON

PRE – LANDING

Airport Information	                 REVIEWED

Seat Belt/Shoulder Harness          TIGHT

Lights		                 AS REQUIRED

Fuel Valve		                 FULLEST TANK

Mixture		                 RICH

Propeller		                 MAX RPM

Brakes		                 FIRM

LANDING

Airspeed Final Approach	85-90 MPH

Flaps (Under 100 MPH)	AS REQUIRED

AFTER LANDING

Flaps			RETRACTED

Lights			AS REQUIRED

SHUTDOWN

Throttle			IDLE

Switches		OFF

Fuel Selector		OFF

Mixture			IDLE C/O

Batt. Master / Alt		OFF

Flaps			DOWN

ENGINE FAILURE DURING FLIGHT

Airspeed		92 MPH

Prop Control		FULL AFT

Landing Site		SELECTED

Mixture			RICH

Fuel Valve		SWITCH TNK

Mag Switches		CHECK

Fuel Pump		ON

AIRSPEEDS

Vx Best Angle Climb	86 MPH

Vy Best Rate Climb		97 MPH

Va Design Maneuvering	116 MPH

Vfe Flap Extend		103 MPH

Vno Max Struc. Cruise	161 MPH

Vne Never Exceed		186 MPH

Best Glide 		92 MPH

Vs Stall Clean 		58 MPH

Vs0 Stall Full Flaps		48 MPH

FORCED LANDING

Radio Call     121.5		AS REQUIRED

Airspeed		75 MPH

Mixture			IDLE C/O

Fuel Valve		OFF

Mag Switches		OFF

Flaps			AS REQUIRED

Batt. Master / Alt		OFF

Doors			UNLATCH

Touchdown		TAIL LOW

Brakes 			AS REQUIRED

ENGINE FIRE IN FLIGHT

Fuel Valve 		OFF

Mixture			IDLE C/O

Mag Switches		BOTH OFF

Batt Master / Alt		OFF

Cabin Heat and Air		OFF

Airspeed		FAST

Forced Landing		EXECUTE

ELECTRICAL FIRE IN FLIGHT

Electrical Switches		OFF

Batt. Master / Alt 		OFF

Mag Switches 		BOTH ON

Air Vents		OPEN

Fire Extinguisher		ACTIVATE

Forced Landing		EXECUTE

FIRE DURING ENGINE START

Cranking		CONTINUE

Throttle			FULL OPEN

IF FIRE PERSISTS

Fuel Valve		OFF

All Switches		OFF

Aircraft			EXIT

Fire Extinguisher		OBTAIN

Fire			EXTINGUISH

COMMUNICATION FREQUENCIES

OAK HARBOR		122.8

PAINE ATIS		128.65

PAINE GROUND		121.80

PAINE TOWER (WEST)	132.95

PAINE TOWER (EAST)	120.20

BREMERTON		123.05    CONCRETE                     	122.9      WHIDBEY AIRPARK	122.9      MONROE		122.9        SAN JUANS                       	128.25

SKAGIT                               	123.075

SEATTLE CENTER          	128.50

SEATTLE RADIO (FSS)   	122.55

WEATHER FREQUENCIES

BREMERTON         AWOS	121.2

FRIDAY HARBOR  ASOS	135.675

ORCAS		AWOS	135.425

SKAGIT		AWOS	121.125

PIERCE COUNTY   AWOS       	128.575

PORT ANGELES	ASOS	135.175

FLIGHT WATCH                 	122.00

EMERGENCY FREQUENCY

EMERGENCY	121.50

SPECIAL XPONDER CODES

Hijack			7500

Comm Out			7600

Emergency			7700

LIGHT GUN SIGNALS

COLOR     IN FLIGHT    ON GROUND

Stdy Green  Clear to Land   Clear for takeoff

Flsh Green  Return to Land    Clear to Taxi

Stdy Red        Give Way               Stop

Flsh Red      Airport Unsafe    Exit Runway

Flsh White           N/A             Return to Start

Alt Red/Green    Exercise Extreme Caution

GENERATOR / ELECTRICAL FAILURE

Non-Essential Equipment	OFF

Master Switch		ON

Flight			TERMINATE

Checklist for N83JD VAN’S RV-8

DITCHING

Forced Landing Procedure	EXECUTE

Flaps			UP

Land into wind or parallel to swells if calm

Contact water in nose high attitude

Exit aircraft immediately

POST TAKE OFF-Once Obstacles Cleared

Throttle			25"

Prop			2500 RPM